## Slide 1: Mosquito
exTorr RGA interface

## Slide 2: Instrument
exTorr RGA Model XT100 http://www.extorr.com/products
Mass range: 1 to 100 amu
Interaction only with Windows
  Control software: Vacuum Plus

## Slide 3: How mosquito works
Behavior of the RGA controlled by instances of VacuumPlus.exe and a set of configuration files loaded by each instance
  Filament off/Saving off (off)
  Filament on/Saving off (warmup)
  Filament on/Saving on (acquisition mode)
Interface with dripline-labview

## Slide 4: Requirements

## Slide 5: Global scheme (main.vi)
Init
.project8_authentications
Config file
Listen to broadcast
broadcast.ping
rga_interface.ping
Listener
- rga_interface.start
Listener
- rga_interface.stop
Listener
- rga_interface.is_running
Display log
Do data taking procedure
Stop taking procedure
Scheduler
Dripline interface
Internal
One-time method
While loop

## Slide 6: Init
Read information from various files and fill some global variables
  Config file for mosquito Config_infos
  .project8_authentications.json (%HOME) AMQP_credentials (dripline-labview)
  Dripline_info (dripline-labview) Sender_info (dripline-labview)

## Slide 7: Broadcast
Stand-alone application
  dripline-labview/vi/API/Listen and reply broadcast.ping.vi
Listen to broadcast.ping and service_name.ping
Possess its own logger
Open and run into a sub-panel of main.vi

## Slide 8: Listeners
Listen to rga_interface_xxx
  Upon receiving a request, check the status of the instrument (is_running)
Reply immediately to any request